## Slide 1: Microcomputer Principles & Computer Interface
Lu Yin
luyin@nwpu.edu.cn

## Slide 2: Chapter 1 The X86 Microprocessor
Contains
  The history of X86 family
  The internal instructions of X86 quick view
  Programming in assembly language quick view

## Slide 3: Section1.2 Inside the 8086
Category | Bits | Register Names
General | 16 | AX,BX,CX,DX
 | 8 | AH,AL,BH,BL,CH,CL,DH,DL
Pointer | 16 | SP(stack pointer), BP(base pointer)
Index | 16 | SI(source index), DI(destination index)
Segment | 16 | CS(code), DS(data), SS(stack), ES(extra)
Instruction | 16 | IP(instruction pointer)
Flag | 16 | FR(flag register)

## Slide 4: Section 1.3 Introduction to Assembly programming
Why is assembly language developed?
  It is difficult for us to read and write in machine language;
What is assembly language?
  Assembly language is a set of mnemonics (codes and abbreviations) for the machine code instructions, plus other grammars.
Typical features of assembly language
  Low level language. It deals directly with the internal structure of the CPU.

## Slide 5: Section 1.3 Introduction to Assembly programming
Construction of assembly language instruction
  Mnemonic + operand/operands
  eg.
  MOV destination, source ;copy source operand ;to destination

## Slide 6
Three rules in using MOV instruction
  The size of operands must match each other;
    Eg. MOV AX, 58FCH
  Only values in registers can be moved into segment registers;
    Eg. MOV DS, 3F47H
    Eg. MOV DX, 3F47H; MOV DS, DX;
  Can not move an operand from memory to memory directly;
    Eg. MOV [0014], [0016];
    Eg. MOV AL, [0016]; MOV [0014], AL

## Slide 7: Section 1.3 Introduction to Assembly programming
Mnemonic | Operands | function
MOV | CL,55H | ;move 55H into register CL
MOV | DL,CL | ;copy the contents of CL into DL
MOV | CX,468FH | ;move 468H into register CX
MOV | AX,2FE456H | ;move 2fe456h into AX (illegal)
MOV | DI,BX | ;copy contents of BX into DI
MOV | BP,2459H | ;move 2459H into register BP (legal)
MOV | DS,2341H | ;move 2341H into DS (illegal)
MOV | DS,AX | ;copy contents of AX into DS (legal)
Nonsegment register
Segment register
Too large

## Slide 8: Section 1.3 Introduction to Assembly programming
MOV MOV ADD | AL, 25H BL, 34H AL, BL | ;move 25 into AL ;move 34 into BL ;AL = Al + BL
MOV ADD | AX, 34EH AX, 65AH | ;move 34EH into AX ;AX = AX + 65AH
The ADD instruction:
ADD destination, source
It adds up source operand to the destination, and
save result in the destination

## Slide 9: Section 1.4 Introduction to Program Segments
Three parts of typical assembly language program
  Code Segment -- contains the assembly language instructions that perform the tasks
  Data Segment – store information that needs to be processed by the instructions in the CS
  Stack Segment – used by the CPU to store information temporarily

## Slide 10: Section 1.4 Introduction to Program Segments
Origin and definition of the segment
  A segment is an area of memory that includes up to 64K bytes and begins on an address evenly divisible by 16 (addr. ends in 0H);
  8-bit processor can only locate 64K bytes;
  16-bit 8086/8088 can locate 1M bytes (20-bit address bus), and assigns each segment 64K bytes;
How to move the 64K window to cover 1M?
  Logical address vs. Physical address
  Logical address converting

## Slide 11: Section 1.4 Introduction to Program Segments
Logical address and Physical address
  There are three types of addresses mentioned in Intel literature
    Physical address – 20-bit address been put on the address pins; ranges from 00000H to FFFFFH;
    offset address – a location within a 64K-byte segment; it ranges from 0000H to FFFFH;
    logical address – consists of a segment value and an offset address , eg. in the code segment, a logical address for an instruction is CS:IP

## Slide 12: Section 1.4 Introduction to Program Segments
Code Segment
  CS(code segment):IP(instruction pointer)
Physical address = CS << 1 + IP
  phy addr. = (2500H << 1) + (95F3H)
  = 25000H + 95F3H
  = 2E5F3H

## Slide 13: Section 1.4 Introduction to Program Segments
Example 1-1
  If CS=24F6H and IP=634AH,
    (a) show the logical address;
    (b) show the offset address;
    (c) calculate the physical address;
    (d) show the lower range of the code segment;
    (e) show the upper range of the code segment.

## Slide 14: Section 1.4 Introduction to Program Segments

## Slide 15: Section 1.4 Introduction to Program Segments

## Slide 16: Section 1.4 Introduction to Program Segments
In order of make the program capable of processing various data sets, an area of memory is set aside strictly for data. Thus data segment is created.
Most data values of operands is stored in data segment.
  The operand is the a part of assembly language instruction, and it use various addressing modes to address the data values stored in the data segment.
Data segment register (DS) is used in calculating physical address of data values.

## Slide 17: Section 1.4 Introduction to Program Segments
Data Segment
  DS(data segment):offset
Physical address = DS << 1 + offset
  phy addr. = (0200H << 1) + (0201H)
  = 02000H + 0201H
  = 02201H

## Slide 18: Section 1.4 Introduction to Program Segments
Example 1-3
  If DS=7FA2H and offset=483EH,
    (a) calculate the physical address;
    (b) calculate the lower range;
    (c) calculate the upper range;
    (d) show the logical address;

## Slide 19: Section 1.4 Introduction to Program Segments
The following program try to calculate the sum of set of data. However, all the data values is build into source codes, and stored in the code segment.
As a result, this program can not be reused to process an other set of data, unless re-write the source code and re-assemble the program.
MOV AL,0 ;clear AL
MOV AL, 25H; load first data into AL
ADD AL,12H; add 12H to AL
ADD AL, 15H
ADD AL, 1FH;
ADD AL, 2BH

## Slide 20
The architecture of modern computers
  John von Neumann Architecture
    Programs are stored in the memory;
    The instructions are executed one after another;
  Protected Mode
    Memory blocks are authorized with different accessing privileges;
    Thus the program segments can not be modified during execution.

## Slide 21: Section 1.4 Introduction to Program Segments
The program can be modified into the following mode:
  All the data needs to be processed is stored in the data segment;
  Data pointer is used in the program to access the data value;
  In such a procedure, different set of data can be processed with the same program by changing data segment register.
DS:0200 = 25
DS:0201 = 12
DS:0202 = 15
DS:0203 = 1F
DS:0204 = 2B
MOV AL,0 ;clear AL
ADD AL,[0200] ;add 12 to AL
ADD AL,[0201]
ADD AL,[0202]
ADD AL,[0203]
ADD AL,[0204]

## Slide 22: Section 1.4 Introduction to Program Segments
And moreover, if regard the data as a byte array, the program can be re-write in the following mode:
  A register is used as a pointer, and holds the offset address;
  After each round of addition, the pointer is moved to point at the next member;
  BX, SI or DI is suggested to be used as the pointer register.
MOV AL,0 ;clear AL
MOV BX, 0200H; set BX points to offset addr of 1st byte
ADD AL, [BX] ; add 1st byte (25H) to AL INC BX; move BX and points to next byte
ADD AL, [BX] INC BX;
(and so on)
DS:0200 = 25
DS:0201 = 12
DS:0202 = 15
DS:0203 = 1F
DS:0204 = 2B

## Slide 23: Section 1.4 Introduction to Program Segments
Example 1-5
  Assume memory locations with the following contents: DS:6826=48 and DS:6827=22, show the contents of register BX in the instruction “MOV BX,[6826]”
There are different data types in x86 assembly language, eg. Byte, word, double word.
While memory space is byte addressed. How does variant greater than a byte stored in the memory?

## Slide 24: Section 1.4 Introduction to Program Segments
Little endian convention
  The high byte goes to the high address, and low byte goes to the low address;
  Intel microprocessors
Big endian convention
  The high byte goes to the low address;
  Freescale (MOTOROLA) POWER PC processors
  JAVA

## Slide 25: Section 1.4 Introduction to Program Segments
Extra segment (ES)
  ES is a segment register used as an extra data segment;
  Its use is absolutely essential for string operations, eg. String operating instructions

## Slide 26: Section 1.4 Introduction to Program Segments
The allocation of the entire memory space is called a memory map.
The memory map of IBM PC:
  The allocation of the 1M memory space is called Memory Map;
  RAM can be used by both the operating system and user applications;

## Slide 27: Section 1.4 Introduction to Program Segments
Video RAM
  The actual space and location of RAM reserved for video depends on the video board installed.
ROM
  64K bytes used by the BIOS program;
  Others reserved for adapter cards;
Function of BIOS ROM
  The PC needs permanent memory to hold the programs that tells the CPU what to do during the power on period.
  BIOS (Basic Input-Output System): Contains programs to test RAM and other components connected to the CPU, combined with programs that allow operating system to communicate with peripheral devices.

## Slide 28: Review
00000H
FFFFFH
Our Programs
10000H
20000H
35000H
0000H
FFFFH
Question:
What if the difference between two segment address is little than 64K ?

## Slide 29: Section 1.4 Introduction to Program Segments
Overlapping
  A single physical address belong to more than one segments.
  It often happens between DS and SS
Danger: Stack size declaration too small is very dangerous in recursive function calling programs. Overlapping may damage the data, or even the program!

## Slide 30: Section 1.5 The Stack
What is a stack, and why is it needed?
  Stack is a piece of RAM space used by the CPU to store information temporarily;
  It is a supplement of internal registers;
  The payment of using stack instead of registers is much longer access time.

## Slide 31: Section 1.5 The Stack
How Stacks are accessed
  SS (Stack Segment register) and SP (Stack Pointer register); BP (Base Pointer reg)
  Push operation push one register value (16-bit) onto the stack; the SP decreases by 2;
  Pop operation popped a value in stack off, and store it into a register; the SP increases by 2;
  Most in the case, CS and SS are located at opposite ends of he RAM memory.

## Slide 32: Section 1.5 The Stack
Example 1-6
  Assuming that SP=1236, DI=85C2, DX=5F93, AX=24B6. show the contents of the stack as each of the following instructions is executed.
PUSH AX
PUSH DI
PUSH DX

## Slide 33: Allocation of program segments
00000H
FFFFFH
Our Programs
10000H
10E00H
20E00H
0000H
FFFFH
Most in the case, CS and SS are located at opposite ends of he RAM memory.
And in Model Small of assemble, memory space allocated are always depressed. SS, DS and CS will share a block of physical memory, and overlap each other.

## Slide 34: Stack in sub function calling
Int do_sum(int* num, int len);
Main()
{
int ary_cost[5] = {12,13,14,15,16};
int sum = 0;
do_sum(ary_cost); //CS:IP = CS:0010;
printf(“The total cost is: %d”, sum); //CS:IP=0014
}
Int do_sum(int* num, int len)
{
int result = 0;
for(int i=0; i<len; i++)
{
result=result + num[i];
}
return result;
}

## Slide 35: Section 1.6 Flag Register
The FS is used to indicate the processor’s status, or to control the operation of some instructions;
Conditional flags: CF, PF, AF, ZF, SF, OF;
Control flags:DF, IF, TF.

## Slide 36: Section 1.6 Flag Register
CF (carry flag): a carry out from d7 or d15;
PF (parity flag): set PF to make the number of 1s in a byte odd;
AF (Auxiliary carry flag): a carry out from d3 to d4 (often used in BCD arithmetic);
ZF (zero flag): result is zero;
SF (sign flag): result is negative (MSB is “1”);
TF (trap flag): allows the program to single-step;
IF (interrupt flag): enables external maskable interrupt requests;
DF (direction flag): direction of string scanning;
OF (overflow flag): the result of a signed number operation is to large, casuing the high-order bit to overflow into the sign bit.

## Slide 37: Section 1.6 Flag Register
Example 1-10
  Show how the flag register is affected by the addition of 38H and 2FH
  CF = 0 since there is no carry beyond d7
  AF = 1 since there is carry from d3 to d4
  PF = 0 since there is an odd number of 1s in the result
  ZF = 0 since the result is not zero
  SF = 0 since d7 of the result is zero

## Slide 38: Section 1.6 Flag Register
Example 1-13
  Show how the flag register is affected by the addition of 34F5H and 95EBH
  CF = 0 since there is no carry beyond d15
  AF = 1 since there is carry from d3 to d4
  PF = 0 since there is an odd number of 1s in the lower byte
  ZF = 0 since the result is not zero
  SF = 1 since d15 of the result is not zero

## Slide 39: Section 1.7 x86 Addressing Modes
Addressing Modes: the way the CPU access its operands;
They are determined when the processor is designed, and can not be changed.
7 addressing modes of x86 processor:
  Register - based relative
  Immediate - indexed relative
  Direct - based indexed relative
  Register indirect

## Slide 40: Section 1.7 x86 Addressing Modes
Register addressing mode
  Use registers to hold the data to be manipulated.
  No memory access.
  Eg.
    MOV BX, DX ;both operands are register addressing

## Slide 41: Section 1.7 x86 Addressing Modes
Immediate addressing mode
  The source operand is a constant.
  After assembling, the operand comes immediately after the opcode.
  Eg.
    MOV AX, 2550H
  Besides register and immediate addressing mode, the operand resident in the data segment memory space in the other addressing modes.

## Slide 42: Section 1.7 x86 Addressing Modes
Direct addressing mode
  The data locates in the memory space.
  The address of the operand comes immediately after the instruction.
  The address number is the offset within data segment.
  Eg.
    MOV DL, [2400] ;move contents of DS:2400 into DL
    pp47, Example1-15.
    The address number is the offset within data segment.
  In this case the physical address is calculated by the data fallows the opcode with DS .
  Both the source and destination operand may use direct addressing mode.

## Slide 43: Section 1.7 x86 Addressing Modes
Register indirect addressing mode
  The address of the memory location where the operand resides is held by a register.
  The value in the register is the offset within DS.
  Register used in register indirect addressing mode are SI, DI and BX.
  Eg.
    MOV BX, 2400H ; move address 2400H into BX
    MOV AL, [BX] ; load AL with the data resides in [240
  In this case the physical address is calculated by the value hold by the register with DS

## Slide 44: Section 1.7 x86 Addressing Modes
Based relative addressing mode
  Effective address is calculated with the displacement and base address held by BX or BP;
  Fixed combinations are : DS with BX, and SS with BP;
  Eg.
    MOV CX, [BX] + 10
    MOV AL,[BP]+5
  The physical address is calculated as follows:
    PA = Seg<<1 + (base + displacement)
;move DS:BX+10 and DS:BX+10+1 into CX
;PA = DS<<1 + BX + 10
;PA = SS <<1 + BP+ 5

## Slide 45: Section 1.7 x86 Addressing Modes
Indexed relative addressing mode
  Effective address is calculated with the displacement and offset address held by DI or SI;
  The default segment is DS; in some cases, ES is also used as the segment register in indexed relative addressing mode.
  Eg.
    MOV DX, [SI]+5 ;PA = DS<<1 + SI + 5
    MOV CL, [DI]+20 ;PA = DS<<1 + DI + 20
  The physical address is calculated as follows:
    PA = Seg<<1 + (offset + displacement)

## Slide 46: Section 1.7 x86 Addressing Modes
Based indexed addressing mode
  It is a combination of based relative and indexed relative addressing mode
  One base register and one index register is used, thus the physical address is calculated as follows
    PA = (default segment<<1) + base address + offset value + displacement
  If BP is used as the based address register, SS will be used as the segment register, otherwise, DS.
  Eg.
    MOV CL, [BX][DI]+8 ; PA=DS<<1 + BX + DI + 8
    MOV CL, [BP][SI]+12 ; PA=SS<<1 + BP + SI + 12

## Slide 47: How to:
Based relative addressing mode or Indexed relative addressing mode?
  Based relative addressing mode is used if you know exactly the displacement;
  For example, accessing a member reside in the stack, when you know how many registers have been pushed into stack after that member.
Suppose that 3 register has been pushed into stack when calling a sub routine.
[push IP]
[push CS]
PUSH AX
PUSH BX
PUSH CX
And now, you want to load data belong to AX while do not pop out other registers.
MOV BP, SP; ?why not use BX
MOV AX, [BP+4]; ?why the displacement is 4?

## Slide 48: How to:
Based relative addressing mode or Indexed relative addressing mode?
  Indexed relative addressing mode is used in accessing only a part of members inside an array;
  Or scan an array from tail back to head;
Suppose that a byte array is defined in the DATA segment.
.DATA
my_array DB 0,1,2,3,4,5,6,7,8,9
the_sum DB ?
And now, we want to adds them up .
MOV SI, 0
MOV CX, 9;
MOV AL, 0
LOOP1: ADD AL, [SI] ;use SI with displacement value 0
INC SI; ;increase index SI
DEC CX; ;decrease loop counter
JNZ LOOP1 ;loop test
MOV the_sum, AL

## Slide 49: How to:
Based indexed relative addressing mode
  In the example above, what if the array is not reside at the beginning of the DATA segment;
  In such a scenario, the offset address is hard to know.
Suppose that two byte array is defined in the DATA segment.
.DATA
temp_array DB 2,3,4, a, c
my_array DB 0,1,2,3,4,5,6,7,8,9
the_sum DB ?
And now, we want to adds them up .
MOV SI, 0
MOV BX, OFFSET my_array
MOV CX, 9;
MOV AL, 0
LOOP1: ADD AL,[BX][SI];use BX+SI with displacement 0
INC SI; ;increase index SI
DEC CX; ;decrease loop counter
JNZ LOOP1 ;loop test
MOV the_sum, AL

## Slide 50: Section 1.7 x86 Addressing Modes
The combination of segment register and offset register have fixed pairs, as shown in the following table:
Offset registers for various segments
Segment Registers | CS | DS | ES | SS
Offset Registers | IP | SI, DI, BX | SI, DI,BX | SP, BP

## Slide 51: Section 1.7 x86 Addressing Modes
Summary of the X86 addressing modes (pp50 Table1-7)
Addressing Mode | Operand | Default Segment
Register | Reg | None
Immediate | Data | None
Direct | [offset] | DS
Register indirect | [BX][SI] [DI] | DS
Based relative | [BX]+disp [BP]+disp | DS SS
Indexed relative | [DI]+disp [SI]+disp | DS SS
Based indexed relative | [BX][SI]+disp [BX][DI]+disp [BP][SI]+disp [BP][DI]+disp | DS DS SS SS

## Slide 52: Little endian vs. Big endian
Suppose that you are required to monitor the temperature of a electric furnace. The furnace is probed by a thermocouple sensor(热电偶) . And the output of the sensor is sampled via a AD expansion card, which is 32bit ARM based. Your application program is required to be running in Windows platform with a Intel processor, and the device driver of the AD card is developed with C++.
The output of AD conversion is a 24bits integer, and is put into a dual ports buffer under the control of the ARM embedded processor in big endian format. On the other side, the conversion result is read out from the dual port buffer by the host computer which is intel processor based.
Please design a algorithm to acquire the temperature sample result properly.

## Slide 54: Exercise for Chapter 1
Problems:
  Section 1.3: 12
  Section 1.4: 14
  Section 1.7: 34