## Slide 1: Microcomputer Principles & Computer Interface
Lu Yin
luyin@nwpu.edu.cn

## Slide 2: Chapter 15 Direct Memory Access and DMA Channels in x86 PC
Contains
  Describe the concept of DMA
  Explain how bus arbitration is achieved between DMA and the CPU
  Introduction of DMA controller 8237A
  Explain how the channels of the 8237 are used in the PC

## Slide 3: Section 1: Concept of DMA
What is DMA?
  DMA is the abbreviation of Direct Memory Access, which describe the data transfer process between memory and peripheral devices under the control a special device called DMA controller.
    DMA provides direct connection between memory and device for high speed data transfer;
    DMA process is under the control of DMAC, but not CPU.
    DMA process do not need the assistant of CPU; while the preparation for DMA needs help of CPU;
    The CPU will loss control of local bus during DMA process.

## Slide 4: Section 1: Concept of DMA
Scenario: Output 4 bytes to the buffer of a peripheral device.
Why we need DMA?
Traditional solution:
 | Instructions | Number of Clocks
BACK: | MOV AL, [SI] | 10
 | OUT PORT, AL | 10
 | INC SI | 2
 | LOOP BACK | 17
Clocks taken for 1 byte transfer |  | 39
Total clocks for 4 bytes |  | 39*4=156
DMA solution:
 | Instructions | Number of Clocks
 | MOV AX, 3400H | 10
 | OUT DMA_PORT1, AL | 10
 | MOV AL, AH | 2
 | OUT DMA_PORT1, AL | 10
 | MOV AX, 0004 | 10
 | OUT DMA_PORT2, AL | 10
 | MOV AL, AH | 2
 | OUT DMA_PORT2, AL | 10
 | (wait for 4 byte transfer) | 4 * 4
Total clocks for 4 bytes |  | 64+16=80

## Slide 5: Section 1: Concept of DMA
Generally, the processor takes control of the local bus.
Because DMA will transfer data between memory and devices, and memory is connected to the local bus directly, the DMAC needs to take control of local bus.
So, the processor have to give permission to DMAC to use the local bus.
DAMC use signals like HRQ(hold request), HLDA(hold acknowledge), to apply and acknowledge the control of local bus. (See Figure15-1 DMA usage of system bus @ pp403, and Figure 15-14 DMA memory read and IO write bus cycle timing @ pp420)
The apply and acknowledge process is called “Bus Arbitration”
Who takes control of the local bus?

## Slide 6
Device ask for DMA transport. DREQ send to DMAC;
DMAC detects DREQ and send HRQ to CPU;
After the present bus cycle, CPU response Hold Request, and send HLDA to DMAC;
When HLDA is active, CPU give up control of the local bus;
DMAC detects HLDA, then send DACK to the device, and begin the DMA process;
When things are done, DMAC will cancel HRQ and return bus control to CPU.
Bus arbitration process:
1
2
3
4
4
4
5
6

## Slide 7
Device ask for DMA transport. DREQ send to DMAC;
DMA transfer timing (Memory read from IO port, 1 byte):

## Slide 8
DMA process takes 3 stages:
  Preparation: The CPU should initialize the DMAC.
    DMA channel
    One or more bytes transfer
    Data flow direction (in or out memory)
    Starting address, and counts of bytes.
    Index increasing or decreasing
  Bus arbitration: communicate with CPU and take control of local bus.
  Ends up cleaning : notify the device that DMA process is over. So as to cancel DREQ.
Section 1: Concept of DMA